rosshutdown;
clc;
clear;
rosinit('192.168.11.123');
% rosinit('172.29.64.201'); % Ip address
% To establish connection
soundpub=rospublisher('/mobile_base/commands/sound','kobuki_msgs/Sound');
soundmsg = rosmessage(rostype.kobuki_msgs_Sound);
soundmsg.Value=6;
send(soundpub,soundmsg)
robot=rospublisher('/mobile_base/commands/velocity');
velmsg=rosmessage(robot);
laser=rossubscriber('/scan');
tic;
while toc<100
  % Collect information from laser scan
  scan=receive(laser,3);
  plot(scan);
  data=readCartesian(scan);
  x=data(:,1);
  y=data(:,2);
  % Compute distance of the closest obstacle
  dist=sqrt(x.^2+y.^20);
  minDist=min(dist);
  % * Set some parameters that will be used in the processing loop. You can modify
% these values for different behavior.
  spinVelocity=0.6;
  forwardVelocity=0.1;
  backwardVelocity=-0.02;
  distanceThreshold=0.6;
   % Command robot action
  if minDist< distanceThreshold
       % If close to obstacle, back up slightly and spin
      velmsg.Angular.Z=spinVelocity;
      velmsg.Linear.X=backwardVelocity;
  else
        % Continue on forward path
       velmsg.Linear.X=forwardVelocity;
       velmsg.Angular.Z=0;
  end
  send(robot,velmsg);
end